## Slide 1: ECEN 615 Methods of Electric Power Systems Analysis
Lecture 10: Sparse Systems
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Read Chapter 7 from the book
Homework 2 is due today
Homework 3 should be done before the exam put does not need to be turned in
First exam is Tuesday October 8 in class; closed book, closed notes. One 8.5 by 11 inch note sheet and calculators allowed

## Slide 3
Example: 7 by 7 Matrix
Consider the 7 x 7 matrix A with the zero-nonzero pattern shown in (a): of the 49 possible elements there are only 31 that are nonzero
If elimination proceeds with the given ordering, all but two of the 18 originally zero entries, will fill in, as seen in (b)

## Slide 4
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | X | X | X | X | X | X | 
2 | X | X | X |  |  | X | X
3 | X | X | X |  |  | X | X
4 | X |  |  | X | X |  | 
5 | X |  |  | X | X | X | 
6 | X | X | X |  | X | X | 
7 |  | X | X |  |  |  | X
  The original zero-nonzero structure
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | X | X | X | X | X | X | 
2 | X | X | X | F | F | X | X
3 | X | X | X | F | F | X | X
4 | X | F | F | X | X | F | F
5 | X | F | F | X | X | X | F
6 | X | X | X | F | X | X | F
7 |  | X | X | F | F | F | X
The post- elimination zero nonzero pattern
r
c
r
c
Example: 7 by 7 Matrix Structure

## Slide 5
We next reorder the rows and the columns of A so as to result in the pattern shown in (c)
For this reordering, we obtain no fills, as shown in the table of factors given in (d )
In this way, we preserve the original sparsity of A
Example: 7 by 7 Matrix Reordering

## Slide 6
 | 4 | 5 | 1 | 6 | 7 | 3 | 2
4 | X | X | X |  |  |  | 
5 | X | X | X | X |  |  | 
1 | X | X | X | X |  | X | X
6 |  | X | X | X |  | X | X
7 |  |  |  |  | X | X | X
3 |  |  | X | X | X | X | X
2 |  |  | X | X | X | X | X
The reordered system
 | 4 | 5 | 1 | 6 | 7 | 3 | 2
4 | X | X | X |  |  |  | 
5 | X | X | X | X |  |  | 
1 | X | X | X | X |  | X | X
6 |  | X | X | X |  | X | X
7 |  |  |  |  | X | X | X
3 |  |  | X | X | X | X | X
2 |  |  | X | X | X | X | X
The post- elimination reordered system
r
c
r
c
Example: 7 by 7 Matrix Reordered Structure

## Slide 7: Sparse Matrix Reordering
There is no computationally efficient way to optimally reorder a sparse matrix; however there are very efficient algorithms to greatly reduce the fills
Two steps here: 1) order the matrix, 2) add fills
A quite common algorithm combines ordering the matrix with adding the fills
The two methods discussed here were presented in the 1963 paper by Sato and Tinney from BPA; known as Tinney Scheme 1 and Tinney Scheme 2 since they are more explicitly described in Tinney’s 1967 paper
  1967 paper also has Tinney Scheme 3 (briefly covered)
6

## Slide 8: Tinney Scheme 1
Easy to describe, but not really used since the number of fills, while reduced, is still quite high
In graph theory the degree (or valence or valency) of a vertex is the number of edges incident to the vertex
Order the nodes (buses) by the number of incident branches (i.e., its valence) those with the lowest valence are ordered first
  Nodes with just one incident line result in no new fills
  Obviously in a large system many nodes will have the same number of incident branches; ties can be handled arbitrarily
7

## Slide 9: Tinney Scheme 1, Cont.
Once the nodes are reordered, the fills are added
  Common approach to ties is to take the lower numbered node first
A shortcoming of this method is as the fills are added the valence of the adjacent nodes changes
1
2
3
4
5
6
7
8
Tinney 1 order is 1,2,3,7,5,6,8,4
Number of new branches is 2 (4-8, 4-6)
8

## Slide 10: Tinney Scheme 2
The Tinney Scheme 2 usually combines adding the fills with the ordering in order to update the valence on-the-fly as the fills are added
As before the nodes are chosen based on their valence, but now the valence is the actual valence they have with the added lines (fills)
  This is also known as the Minimum Degree Algorithm (MDA)
  Ties are again broken using the lowest node number
This method is quite effective for power systems, and is highly recommended; however it is certainly not guaranteed to result in the fewest fills (i.e. not optimal)
9

## Slide 11: Tinney Scheme 2 Example
Consider the previous network:
Nodes 1,2,3 are chosen as before. But once these nodes are eliminated the valence of 4 is 1, so it is chosen next. Then 5 (with a new valence of 2 tied with 7), followed by 6 (new valence of 2), 7 then 8.
1
2
3
4
5
6
7
8
10

## Slide 12: Coding Tinney 2
The following slides show how to code Tinney 2 for an n by n sparse matrix A
First we setup linked lists grouping all the nodes by their original valence
vcHead is a pointer vector [0..mvValence]
  If a node has no connections its incidence is 0
  Theoretically mvValence should be n-1, but in practice a much smaller number can be used, putting nodes with valence values above this into the vcHead[mvValence] is
11

## Slide 13: Coding Tinney 2, cont.
Setup a boolean vectors chosenNode[1..n] to indicate which nodes are chosen and BSWR[1..n] as a sparse working row; initialize both to all false
Setup an integer vector rowPerm[1..n] to hold the permuted rows; initialize to all zeros
For i := 1 to n Do Begin
  Choose node from valence data structure with the lowest current valence; let this be node k
    Go through vcHead from lastchosen level (last chosen level may need to be reduced by one during the following elimination process;
  Set rowPerm[i] = k; set chosenNode[k] = true
12

## Slide 14: Coding Tinney 2, cont.
  Modify sparse matrix A to add fills between all of k’s adjacent nodes provided
      a branch doesn’t already exist
      both nodes have not already been chosen (their chosenNode entries are false)
    These fills are added by going through each element in row k; for each element set the BSWR elements to true for the incident nodes; add fills if a connection does not already exist (this requires adding two new elements to A)
  Again go through row k updating the valence data structure for those nodes that have not yet been chosen
    These values can either increase or go down by one (because of the elimination of node k)
13

## Slide 15: Coding Tinney 2, cont.
This continues through all the nodes; free all vectors except for rowPerm
At this point in the algorithm the rowPerm vector contains the new ordering and matrix A has been modified so that all the fills have been added
  The order of the rows in A has not been changed, and its columns are no longer sorted
14

## Slide 16: Coding Tinney 2, cont
Sort the rows of A to match the order in rowPerm
  Surprising sorting A is of computational order equal to the number of elements in A
    Go through A putting its elements into column linked lists; these columns will be ordered by row
    Then through the columns linked lists in reverse order given by rowPerm
      That is For i := n downto 1 Do Begin p1 := TSparmatLL(colHead[rowPerm[i]).Head; ….
That’s it – the matrix A is now readying for factoring
Pivoting may be required, but usually isn’t needed in the power flow
15

## Slide 17: Some Example Values for Tinney 2
Number of buses | Nonzeros before fills | Fills | Total nonzeros | Percent nonzeros
37 | 63 | 72 | 135 | 9.86%
118 | 478 | 168 | 646 | 4.64%
18,190 | 64,948 | 31,478 | 96,426 | 0.029%
62,605 | 228,513 | 201,546 | 430,059 | 0.011%
16

## Slide 18: Tinney Scheme 3
“Number the rows so that at each step of the process the next row to be operated upon is the one that will introduce the fewest new nonzero terms.”
“If more than one row meets this criterion, select any one. This involves a trial simulation of every feasible alternative of the elimination process at each step. Input information is the same as for scheme 2).”
Tinney 3 takes more computation and in general does not give fewer fills than the quicker Tinney 2
Tinney got into the NAE in 1998
These are direct quotes from the Tinney-Walker 1967 IEEE Proceedings Paper

## Slide 19: Sparse Forward Substitution with a Permutation Vector
Pass in b in bvector For i := 1 to n Do Begin
k = rowPerm[i]; // this is the only change, except using k
p1 := rowHead[k]; // the row needs to be ordered correctly!
While p1 <> rowDiag[k] Do Begin
bvector[k] = bvector[k] – p1.value*bvector[p1.col];
p1 := p1.next;
End;
End;
18

## Slide 20: Sparse Backward Substitution with Permutation Vector
Pass in b in bvector
For i := n downto 1 Do Begin
k = rowPerm[i];
p1 := rowDiag[k].next;
While p1 <> nil Do Begin
bvector[k] = bvector[k] – p1.value*bvector[p1.col];
p1 := p1.next;
End;
bvector[k] := bvector[k]/rowDiag[k].value;
End;
Note, numeric problems such as matrix singularity are indicated with rowDiag[k].value being zero!
19

## Slide 21: Sparse Vector Methods
Sparse vector methods are useful for cases in solving Ax=b in which
  A is sparse
  b is sparse
  only certain elements of x are needed
In these right circumstances sparse vector methods can result in extremely fast solutions!
A common example is to find selected elements of the inverse of A, such as diagonal elements.
20

## Slide 22: Sparse Vector Methods
Often times multiple solutions with varying b values are required
  A only needs to be factored once, with its factored form used many times
Key reference is
  W.F. Tinney, V. Brandwajn, and S.M. Chan, "Sparse Vector Methods", IEEE Transactions on Power Apparatus and Systems, vol. PAS-104, no. 2, February 1985, pp. 295-300
21