## Slide 1: ECEN 615 Methods of Electric Power Systems Analysis
Lecture 4: Power Flow
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Start reading Chapters 1 to 3 from the book (mostly background material)
Homework 1 is assigned today. It is due on Thursday September 3
Public website is
https://overbye.engr.tamu.edu/ecen-615-fall-2020/

## Slide 3: Using the Ybus
However, this requires that Ybus not be singular; note it will be singular if there are no shunt connections!

## Slide 4: Solving for Bus Currents

## Slide 5: Solving for Bus Voltages

## Slide 6: Power Flow Analysis
When analyzing power systems we know neither the complex bus voltages nor the complex current injections
Rather, we know the complex power being consumed by the load, and the power being injected by the generators plus their voltage magnitudes
Therefore we can not directly use the Ybus equations, but rather must use the power balance equations

## Slide 7: Power Balance Equations

## Slide 8: Power Balance Equations, cont’d

## Slide 9: Real Power Balance Equations

## Slide 10: Power Flow Analysis
When analyzing power systems we know neither the complex bus voltages nor the complex current injections
Rather, we know the complex power being consumed by the load, and the power being injected by the generators plus their voltage magnitudes
Therefore we can not directly use the Ybus equations, but rather must use the power balance equations

## Slide 11: Power Flow Analysis
Classic paper for this lecture is W.F. Tinney and C.E. Hart, “Power Flow Solution by Newton’s Method,” IEEE Power App System, Nov 1967
Basic power flow is also covered in essentially any power system analysis textbooks.
We use the term “power flow” not “load flow” since power flows not load. Also, the power flow usage is not new (see title of Tinney’s 1967 paper, and note Tinney references Ward’s 1956 power flow paper)
  A nice history of the power flow is given in an insert by Alvarado and Thomas in T.J. Overbye, J.D. Weber, “Visualizing the Electric Grid,” IEEE Spectrum, Feb 2001.

## Slide 12: Early Power Flow System Size
In 1957 Bill Tinney, in a paper titled “Digital Solutions for Large Power Networks,” studied a 100 bus, 200 branch system (with 2 KB of memory)!
In Tinney’s 1963 “Techniques for Exploiting Sparsity of the Network Admittance Matrix” paper (which gave us the Tinney Schemes 1, 2, and 3), uses 32 kB for 1000 nodes.
In Tinney’s classic 1967 “Power Flow Solution by Newton’s Method” paper he applies his method to systems with up to about 1000 buses (with 32 kB of memory) and provides a solution time of 51 seconds for a 487 bus system.

## Slide 13: Slack Bus
We can not arbitrarily specify S at all buses because total generation must equal total load + total losses
We also need an angle reference bus.
To solve these problems we define one bus as the "slack" bus. This bus has a fixed voltage magnitude and angle, and a varying real/reactive power injection.
In an actual power system the slack bus does not really exist; frequency changes locally when the power supplied does not match the power consumed

## Slide 14: Three Types of Power Flow Buses
There are three main types of power flow buses
  Load (PQ) at which P/Q are fixed; iteration solves for voltage magnitude and angle.
  Slack at which the voltage magnitude and angle are fixed; iteration solves for P/Q injections
  Generator (PV) at which P and |V| are fixed; iteration solves for voltage angle and Q injection

## Slide 15: Newton-Raphson Algorithm
Most common technique for solving the power flow problem is to use the Newton-Raphson algorithm
Key idea behind Newton-Raphson is to use sequential linearization

## Slide 16: Newton-Raphson Power Flow

## Slide 17: Power Flow Variables

## Slide 18: N-R Power Flow Solution

## Slide 19: Power Flow Jacobian Matrix

## Slide 20: Power Flow Jacobian Matrix, cont’d

## Slide 21: Two Bus Newton-Raphson Example
For the two bus power system shown below, use the Newton-Raphson power flow to determine the voltage magnitude and angle at bus two. Assume that bus one is the slack and SBase = 100 MVA.

## Slide 22: Two Bus Example, cont’d

## Slide 23: Two Bus Example, cont’d

## Slide 24: Two Bus Example, First Iteration

## Slide 25: Two Bus Example, Next Iterations

## Slide 26: Two Bus Solved Values
Once the voltage angle and magnitude at bus 2 are known we can calculate all the other system values, such as the line flows and the generator reactive power output
PowerWorld Case Name: Bus2_Intro
Note, most PowerWorld cases will be available on the course website

## Slide 27: Two Bus Case Low Voltage Solution

## Slide 28: Low Voltage Solution, cont'd

## Slide 29: Practical Power Flow Software Note
Most commercial software packages have built in defaults to prevent convergence to low voltage solutions.
  One approach is to automatically change the load model from constant power to constant current or constant impedance when the load bus voltage gets too low
  In PowerWorld these defaults can be modified on the Tools, Simulator Options, Advanced Options page; note you also need to disable the “Initialize from Flat Start Values” option
  The PowerWorld case Bus2_Intro_Low is set solved to the low voltage solution
  Initial bus voltages can be set using the Bus Information Dialog

## Slide 30: Two Bus Region of Convergence
Slide shows the region of convergence for different initial guesses of bus 2 angle (x-axis) and magnitude (y-axis)
Red region
converges
to the high
voltage
solution,
while the
yellow region
converges
to the low
voltage
solution

## Slide 31: Power Flow Fractal Region of Convergence
Earliest paper showing fractal power flow regions of convergence is by C.L DeMarco and T.J. Overbye, “Low Voltage Power Flow Solutions and Their Role in Exit Time Bases Security Measures for Voltage Collapse,” Proc. 27th IEEE CDC, December 1988
A more widely known paper is J.S. Thorp, S.A. Naqavi, “Load-Flow Fractals Draw Clues to Erratic Behavior,” IEEE Computer Applications in Power, January 1997

## Slide 32: PV Buses
Since the voltage magnitude at PV buses is fixed there is no need to explicitly include these voltages in x or write the reactive power balance equations
  the reactive power output of the generator varies to maintain the fixed terminal voltage (within limits)
  optionally these variations/equations can be included by just writing the explicit voltage constraint for the generator bus |Vi | – Vi setpoint = 0

## Slide 33: Three Bus PV Case Example

## Slide 34: Modeling Voltage Dependent Load

## Slide 35: Voltage Dependent Load Example

## Slide 36: Voltage Dependent Load, cont'd

## Slide 37: Voltage Dependent Load, cont'd
With constant impedance load the MW/Mvar load at
bus 2 varies with the square of the bus 2 voltage
magnitude. This if the voltage level is less than 1.0,
the load is lower than 200/100 MW/Mvar
PowerWorld Case Name: Bus2_Intro_Z

## Slide 38: Generator Reactive Power Limits
The reactive power output of generators varies to maintain the terminal voltage; on a real generator this is done by the exciter
To maintain higher voltages requires more reactive power
Generators have reactive power limits, which are dependent upon the generator's MW output
These limits must be considered during the power flow solution.

## Slide 39: Generator Reactive Limits, cont'd
During the power flow once a solution is obtained there is a check to make sure the generator reactive power output is within its limits
If the reactive power is outside of the limits, fix Q at the max or min value, and resolve treating the generator as a PQ bus
  this is know as "type-switching"
  also need to check if a PQ generator can again regulate
Rule of thumb: to raise system voltage we need to supply more vars

## Slide 40
400 MVA
15 kV
400 MVA
15/345 kV
T1
T2
800 MVA
345/15 kV
800 MVA
15 kV
520 MVA
80 MW
40 Mvar
280 Mvar
800 MW
Line 3 345 kV
Line 2
Line 1
345 kV 100 mi
345 kV 200 mi
50 mi
1
4
3
2
5
Single-line diagram
The N-R Power Flow: 5-bus Example
This five bus example is taken from Chapter 6 of Power System Analysis and Design by Glover, Overbye, and Sarma, 6th Edition, 2016

## Slide 41
Bus | Type | V per unit |  degrees | PG per unit | QG per unit | PL per unit | QL per unit | QGmax per unit | QGmin per unit
1 | Swing | 1.0 | 0 |  |  | 0 | 0 |  | 
2 | Load |  |  | 0 | 0 | 8.0 | 2.8 |  | 
3 | Constant voltage | 1.05 |  | 5.2 |  | 0.8 | 0.4 | 4.0 | -2.8
4 | Load |  |  | 0 | 0 | 0 | 0 |  | 
5 | Load |  |  | 0 | 0 | 0 | 0 |  | 
Table 1.
Bus input
data
Bus-to-Bus | R’ per unit | X’ per unit | G’ per unit | B’ per unit | Maximum MVA per unit
2-4 | 0.0090 | 0.100 | 0 | 1.72 | 12.0
2-5 | 0.0045 | 0.050 | 0 | 0.88 | 12.0
4-5 | 0.00225 | 0.025 | 0 | 0.44 | 12.0
Table 2.
Line input data
The N-R Power Flow: 5-bus Example
Notes: 40

## Slide 42
Bus-to-Bus | R per unit | X per unit | Gc per unit | Bm per unit | Maximum MVA per unit | Maximum TAP Setting per unit
1-5 | 0.00150 | 0.02 | 0 | 0 | 6.0 | —
3-4 | 0.00075 | 0.01 | 0 | 0 | 10.0 | —
Table 3.
Transformer
input data
Bus | Input Data | Unknowns
1 | V1 = 1.0, 1 = 0 | P1, Q1
2 | P2 = PG2-PL2 = -8 Q2 = QG2-QL2 = -2.8 | V2, 2
3 | V3 = 1.05 P3 = PG3-PL3 = 4.4 | Q3, 3
4 | P4 = 0, Q4 = 0 | V4, 4
5 | P5 = 0, Q5 = 0 | V5, 5
Table 4. Input data
and unknowns
The N-R Power Flow: 5-bus Example
Notes: 41

## Slide 43
Five Bus Case Ybus
PowerWorld Case Name: GOS_FiveBus
Notes: 42

## Slide 44: Ybus Calculation Details
Elements of Ybus connected to bus 2
Notes: 43

## Slide 45: Initial Bus Mismatches
Notes: 44

## Slide 46: Initial Power Flow Jacobian
Notes: 45

## Slide 47
Hand Calculation Details
Notes: 46

## Slide 48: Five Bus Power System Solved
Notes: 47

## Slide 49: 37 Bus Case Example
PowerWorld Case Name: Aggieland37

## Slide 50: Voltage Control Example: 37 Buses
PowerWorld Case Name: Bus37_VoltageControl

## Slide 51: Power System Operations Overview
Goal is to provide an intuitive feel for power system operation
Emphasis will be on the impact of the transmission system
Introduce basic power flow concepts through small system examples

## Slide 52: Power System Basics
All power systems have three major components: Generation, Load and Transmission/Distribution.
Generation: Creates electric power.
Load: Consumes electric power.
Transmission/Distribution: Transmits electric power from generation to load.
  Lines/transformers operating at voltages above 100 kV are usually called the transmission system. The transmission system is usually networked.
  Lines/transformers operating at voltages below 100 kV are usually called the distribution system (radial).

## Slide 53: Large System Example: Texas 2000 Bus Synthetic System
This case requires the commercial version of PowerWorld since the GOS Version is limited to 42 Buses

## Slide 54: Three Bus PowerWorld Simulator Case
Load with
green
arrows
indicating
amount
of MW
flow
Used
to control
output of
generator
Note the
power
balance at
each bus
Direction of green arrow is used to indicate
direction of real power (MW) flow; the blue arrows show the reactive power
PowerWorld Case Name: B3Slow

## Slide 55: Basic Power Control
Opening a circuit breaker causes the power flow to instantaneously (nearly) change.
No other way to directly control power flow in a transmission line.
By changing generation we can indirectly change this flow.
Power flow in transmission line is limited by heating considerations
Losses (I^2 R) can heat up the line, causing it to sag.

## Slide 56: Modeling Consideration – Change is Not Really Instantaneous!
The change isn’t really instantaneous because of propagation delays, which are near the speed of light; there also wave reflection issues
  This is covered in ECEN 667
Red is the vs end, green the v2 end

## Slide 57: Transmission Line Limits
Power flow in transmission line is limited by heating considerations.
Losses (I2 R) can heat up the line, causing it to sag.
Each line has a limit; many utilities use winter/summer limits.

## Slide 58: Overloaded Transmission Line

## Slide 59: Interconnected Operation Balancing Authority (BA) Areas
North American Eastern and Western grids are divided into balancing authority areas (BA)
  Often just called an area
Transmission lines that join two areas are known as tie-lines.
The net power out of an area is the sum of the flow on its tie-lines.
The flow out of an area is equal to total gen - total load - total losses = tie-flow

## Slide 60: US Balancing Authorities

## Slide 61: Area Control Error (ACE)
The area control error is the difference between the actual flow out of an area, and the scheduled flow
  ACE also includes a frequency component that we will probably consider later in the semester
Ideally the ACE should always be zero
Because the load is constantly changing, each utility (or ISO) must constantly change its generation to “chase” the ACE
ACE was originally computed by utilities; increasingly it is computed by larger organizations such as ISOs

## Slide 62: Automatic Generation Control
Most utilities (ISOs) use automatic generation control (AGC) to automatically change their generation to keep their ACE close to zero.
Usually the control center calculates ACE based upon tie-line flows; then the AGC module sends control signals out to the generators every couple seconds.

## Slide 63: Three Bus Case on AGC
Net tie flow is
close to zero
Generation
is automatically
changed to match
change in load