ECEN 615 Homework 3

Should Be Done Before First Exam

1.	Manually do an LU factorization on the following matrix A.  Then manually do a forward and backward substitution to solve for x in Ax=b

2	Code the LU factorization discussed in class for full matrices, along with the forward/backward substitution. To test your algorithm use it to factor and solve the below matrix from question 1. You do not need to code pivoting.

3.	Use the Tinney 1 approach to order the following network.  Give the permutation vector.

4.	Repeat question 3 using the Tinney 2 approach.

5.	Using your reordered results from question 4, draw the full factorization path graph for the system.

6.	For the B7Flat case (mentioned in class), calculate the dc power flow solution; you can use a matrix package such as Matlab to invert the B matrix.  Verify your result using PowerWorld.

7.	Using your results from problem 6 (and the dc power flow approximation), give the sensitivity of the MW flow on the line going from bus 3 to bus 4 for an increase in the generation at bus 2 (assuming it is all absorbed by the slack bus [bus 7]).

8.	Solve all problems on the ECEN 615 Exam from October 8, 2019