## Slide 1: ECEN 615 Methods of Electric Power Systems Analysis
Lecture 6: Power Operations, Power Flow
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Read Chapter 6 from the book
    The book formulates the power flow using the polar form for the Ybus elements
Homework 2 is due on Thursday September 17

## Slide 3: Three Bus PowerWorld Simulator Case
Load with
green
arrows
indicating
amount
of MW
flow
Used
to control
output of
generator
Note the
power
balance at
each bus
Direction of green arrow is used to indicate
direction of real power (MW) flow; the blue arrows show the reactive power
PowerWorld Case Name: B3Slow

## Slide 4: Basic Power Control
Opening a circuit breaker causes the power flow to instantaneously (nearly) change.
No other way to directly control power flow in a transmission line.
By changing generation we can indirectly change this flow.
Power flow in transmission line is limited by heating considerations
Losses (I^2 R) can heat up the line, causing it to sag.

## Slide 5: Transmission Line Limits
Power flow in transmission line is limited by heating considerations.
Losses (I2 R) can heat up the line, causing it to sag.
Each line has a limit; many utilities use winter/summer limits.

## Slide 6: Overloaded Transmission Line

## Slide 7: Interconnected Operation Balancing Authority (BA) Areas
North American Eastern and Western grids are divided into balancing authority areas (BA)
  Often just called an area
Transmission lines that join two areas are known as tie-lines.
The net power out of an area is the sum of the flow on its tie-lines.
The flow out of an area is equal to total gen - total load - total losses = tie-flow

## Slide 8: US Balancing Authorities

## Slide 9: Area Control Error (ACE)
The area control error is the difference between the actual flow out of an area, and the scheduled flow
  ACE also includes a frequency component that we will probably consider later in the semester
Ideally the ACE should always be zero
Because the load is constantly changing, each utility (or ISO) must constantly change its generation to “chase” the ACE
ACE was originally computed by utilities; increasingly it is computed by larger organizations such as ISOs

## Slide 10: Automatic Generation Control
Most utilities (ISOs) use automatic generation control (AGC) to automatically change their generation to keep their ACE close to zero.
Usually the control center calculates ACE based upon tie-line flows; then the AGC module sends control signals out to the generators every couple seconds.

## Slide 11: Three Bus Case on AGC
Net tie flow is
close to zero
Generation
is automatically
changed to match
change in load

## Slide 12: Generator Costs
There are many fixed and variable costs associated with power system operation
The major variable cost is associated with generation.
Cost to generate a MWh can vary widely
For some types of units (such as hydro and nuclear) it is difficult to quantify
More others such as wind and solar the marginal cost of energy is essentially zero (actually negative for wind!)
For thermal units it is straightforward to determine
Many markets have moved from cost-based to price-based generator costs

## Slide 13: Economic Dispatch
Economic dispatch (ED) determines the least cost dispatch of generation for an area.
For a lossless system, the ED occurs when all the generators have equal marginal costs. IC1(PG,1) = IC2(PG,2) = … = ICm(PG,m)

## Slide 14: Power Transactions
Power transactions are contracts between areas to do power transactions.
Contracts can be for any amount of time at any price for any amount of power.
Scheduled power transactions are implemented by modifying the area ACE: ACE = Pactual,tie-flow - Psched

## Slide 15: 100 MW Transaction
Scheduled 100 MW transaction from the Home Area to the Other Area
Net tie-line
flow is now
100 MW

## Slide 16: Security Constrained ED
Transmission constraints often limit system economic operation.
Such limits required a constrained dispatch in order to maintain system security.
In the three bus case the generation at bus 3 must be constrained to avoid overloading the line from bus 2 to bus 3.

## Slide 17: Security Constrained Dispatch
Dispatch is no longer optimal due to need to keep the line
from bus 2 to bus 3 from overloading

## Slide 18: Multi-Area Operation
If areas have direct interconnections then they may directly transact, up to the capacity of their tie-lines.
Actual power flows through the entire network according to the impedance of the transmission lines.
Flow through other areas is known as “parallel path” or “loop flow.”

## Slide 19: Seven Bus Case: One-line
System has three areas
Area Left
has one
bus
Area Right has one bus
Area Top
has five
buses
PowerWorld Case: B7Flat

## Slide 20: Seven Bus Case: Area View
System has
40 MW of
“Loop Flow”
Actual
flow
between
areas
Scheduled
flow

## Slide 21: Seven Bus - Loop Flow?
100 MW Transaction
between Left and Right
Transaction has actually decreased
the loop flow
Note that
Top’s
losses have
increased
from
7.1 MW to
9.6 MW

## Slide 22: Pricing Electricity
Cost to supply electricity to bus is called the locational marginal price (LMP)
Presently some electric markets post LMPs on the web
In an ideal electricity market with no transmission limitations the LMPs are equal
Transmission constraints can segment a market, resulting in differing LMP
Determination of LMPs requires the solution on an Optimal Power Flow (OPF), which will be covered later in the semester

## Slide 23: Three Bus LMPs – Constraints Ignored
Line from Bus 1 to Bus 3 is over-loaded; all buses have same marginal cost
Gen 1’s
cost
is $10
per
MWh
Gen 2’s
cost
is $12
per
MWh
PowerWorld Case: B3LP

## Slide 24: Three Bus LMPs – Constraint Unforced
Line from 1 to 3 is no longer overloaded, but now
the marginal cost of electricity at bus 3 is $14 / MWh

## Slide 25: MISO LMPs on 9/3/2020, 4:30 PM
Five minute LMPs are posted online for the MISO footprint
Source: https://www.misoenergy.org/markets-and-operations/real-time--market-data/real-time-displays/

## Slide 26: Advanced Power Flow
Next slides cover some more advanced power flow topics that need to be considered in many commercial power flow studies
An important consideration in the power flow is the assumed time scale of the response, and the assumed model of operator actions
  Planning power flow studies usually assume automatic modeling of operator actions and a longer time frame of response (controls have time to reach steady-state)
    For example, who is actually doing the volt/var control
  In real-time applications operator actions are usually not automated and controls may be more limited in time

## Slide 27: Quasi-Newton Power Flow Methods
First we consider some modified versions of the Newton power flow (NPF)
Since most of the computation in the NPF is associated with building and factoring the Jacobian matrix, J, the focus is on trying to reduce this computation
In a pure NPF J is build and factored each iteration
Over the years pretty much every variation of the NPF has been tried; here we just touch on the most common
Whether a method is effective can be application dependent
  For example, in contingency analysis we are usually just resolving a solved case with an often small perturbation

## Slide 28: Quasi-Newton Power Flow Methods
The simplest modification of the NPF results when J is kept constant for a number of iterations, say k iterations
  Sometimes known as the Dishonest Newton
The approach balances increased speed per iteration, with potentially more iterations to perform
There is also an increased possibility for divergence
Since the mismatch equations are not modified, if it converges it should converge to the same solution as the NPF
These methods are not commonly used, except in very short duration, sequential power flows with small mismatches

## Slide 29: Dishonest N-R Example
We pay a price
in increased
iterations, but
with decreased
computation
per iteration; that price is too high in this example

## Slide 30: Decoupled Power Flow
Rather than not updating the Jacobian, the decoupled power flow takes advantage of characteristics of the power grid in order to decouple the real and reactive power balance equations
  There is a strong coupling between real power and voltage angle, and reactive power and voltage magnitude
  There is a much weaker coupling between real power and voltage angle, and reactive power and voltage angle
Key reference is B. Stott, “Decoupled Newton Load Flow,” IEEE Trans. Power. App and Syst., Sept/Oct. 1972, pp. 1955-1959

## Slide 31: Decoupled Power Flow Formulation

## Slide 32: Decoupling Approximation

## Slide 33: Off-diagonal Jacobian Terms
By assuming ½ the elements are zero, we only have to do ½ the computations

## Slide 34: Decoupled N-R Region of Convergence
The high solution ROC is actually larger than with the standard NPF. Obviously this is not a good a way to get the low
solution

## Slide 35: Fast Decoupled Power Flow
By continuing with our Jacobian approximations we can actually obtain a reasonable approximation that is independent of the voltage magnitudes/angles.
This means the Jacobian need only be built/inverted once per power flow solution
This approach is known as the fast decoupled power flow (FDPF)

## Slide 36: Fast Decoupled Power Flow, cont.
FDPF uses the same mismatch equations as standard power flow (just scaled) so it should have same solution
The FDPF is widely used, though usually only when we only need an approximate solution
Key fast decoupled power flow reference is B. Stott, O. Alsac, “Fast Decoupled Load Flow,” IEEE Trans. Power App. and Syst., May 1974, pp. 859-869
Modified versions also exist, such as D. Jajicic and A. Bose, “A Modification to the Fast Decoupled Power Flow for Networks with High R/X Ratios, “IEEE Transactions on Power Sys., May 1988, pp. 743-746

## Slide 37: FDPF Approximations
To see the impact on the real power equations recall

## Slide 38: FDPF Approximations
With the approximations for the diagonal term we get
Hence the Jacobian for the real equations can be approximated as –B

## Slide 39: FPDF Approximations
For the reactive power equations we also scale by Vi
For the Jacobian off-diagonals we get

## Slide 40: FDPF Approximations
And for the reactive power Jacobian diagonal we get
As derived the real and reactive equations have a constant Jacobian equal to –B
  Usually modifications are made to omit from the real power matrix elements that affect reactive flow (like shunts) and from the reactive power matrix elements that affect real power flow, like phase shifters
  We’ll call the real power matrix B’ and the reactive B”

## Slide 41: FDPF Region of Convergence

## Slide 42: FDPF Cautions
The FDPF works well as long as the previous approximations hold for the entire system
With the movement towards modeling larger systems, with more of the lower voltage portions of the system represented (for which r/x ratios are higher) it is quite common for the FDPF to get stuck because small portions of the system are ill-behaved
The FDPF is commonly used to provide an initial guess of the solution or for contingency analysis

## Slide 43: DC Power Flow
The “DC” power flow makes the most severe approximations:
  completely ignore reactive power, assume all the voltages are always 1.0 per unit, ignore line conductance
This makes the power flow a linear set of equations, which can be solved directly
The term dc power flow actually dates from the time of the old network analyzers (going back into the 1930’s)
Not to be confused with the inclusion of HVDC lines in the standard NPF
P sign convention is generation is positive

## Slide 44: DC Power Flow References
I don’t think a classic dc power flow paper exists; a nice formulation is given in our book Power Generation and Control book by Wood, Wollenberg and Sheble
The August 2009 paper in IEEE Transactions on Power Systems, “DC Power Flow Revisited” (by Stott, Jardim and Alsac) provides good coverage
T. J. Overbye, X. Cheng, and Y. Sun, “A comparison of the AC and DC power flow models for LMP Calculations,” in Proc. 37th Hawaii Int. Conf. System Sciences, 2004, compares the accuracy of the approach

## Slide 45: DC Power Flow Example
Example from Power System Analysis and Design, by Glover, Overbye, Sarma, 6th Edition

## Slide 46: DC Power Flow in PowerWorld
PowerWorld allows for easy switching between the dc and ac power flows (case Aggieland37)
To use the dc approach in PowerWorld select Tools, Solve, DC Power Flow
Notice there are no losses

## Slide 47: Modeling Transformers with Off-Nominal Taps and Phase Shifts
If transformers have a turns ratio that matches the ratio of the per unit voltages than transformers are modeled in a manner similar to transmission lines.
However it is common for transformers to have a variable tap ratio; this is known as an “off-nominal” tap ratio
  The off-nominal tap is t, initially we’ll consider it a real number
  We’ll cover phase shifters shortly in which t is complex

## Slide 48: Transformer Representation
The one–line diagram of a branch with a variable tap transformer
The network representation of a branch with off–nominal turns ratio transformer is
k
m
the tap is on
the side of bus k
k
t :1

## Slide 49: Transformer Nodal Equations
From the network representation
Also

## Slide 50: Transformer Nodal Equations
We may rewrite these two equations as
This approach was first presented in F.L. Alvarado, “Formation of Y-Node using the Primitive Y-Node Concept,” IEEE Trans. Power App. and Syst., December 1982
Ybus is still symmetric here (though this will change with phase shifters)

## Slide 51: The p-Equivalent Circuit for a Transformer Branch
k
m

## Slide 52: Variable Tap Voltage Control
A transformer with a variable tap, i.e., the variable t is not constant, may be used to control the voltage at either the bus on the side of the tap or at the bus on the side away from the tap
This constitutes an example of single criterion control since we adjust a single control variable (i.e., the transformer tap t) to achieve a specified criterion: the maintenance of a constant voltage at a designated bus
Names for this type of control are on-load tap changer (LTC) transformer or tap changing under load (TCUL)
Usually on low side; there may also be taps on high side that can be adjusted when it is de-energized

## Slide 53: Variable Tap Voltage Control
An LTC is a discrete control, often with 32 incremental steps of 0.625% each, giving an automatic range of  10%
It follows from the  – equivalent model for the transformer that the transfer admittance between the buses of the transformer branch and the contribution to the self admittance at the bus away from the tap explicitly depend on t
However, the tap changes in discrete steps; there is also a built in time delay in how fast they respond
Voltage regulators are devices with a unity nominal ratio, and then a similar tap range

## Slide 54: Ameren Champaign (IL) Test Facility Voltage Regulators
These are connected on the low side of a 69/12.4 kV transformer; each phase can be regulated separately