## Slide 1: ECEN 460 Power System Operation and Control
Lecture 11: Power Flow
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Read Chapter 6.7 to 6.11
Exam 1 Results: Avg: 78.8
  96-100: 1
  92-95: 1
  88-91: 6
  84-87: 11
  80-83: 14
  76-79: 14
  72-75: 8
  68-71: 7
  67 or less: 6

## Slide 3: Problem 6.25
Use Newton-Raphson to solve

## Slide 4: At the End of Lecture 9 We Had

## Slide 5: NR Application to Power Flow

## Slide 6: Real Power Balance Equations

## Slide 7: Newton-Raphson Power Flow

## Slide 8: Power Flow Variables

## Slide 9: N-R Power Flow Solution

## Slide 10: Power Flow Jacobian Matrix

## Slide 11: Power Flow Jacobian Matrix, cont’d

## Slide 12: Two Bus Newton-Raphson Example
For the two bus power system shown below, use the
Newton-Raphson power flow to determine the
voltage magnitude and angle at bus two. Assume
that bus one is the slack and SBase = 100 MVA.

## Slide 13: Two Bus Example, cont’d

## Slide 14: Two Bus Example, cont’d

## Slide 15: Two Bus Example, First Iteration

## Slide 16: Two Bus Example, Next Iterations

## Slide 17: Two Bus Solved Values
Once the voltage angle and magnitude at bus 2 are
known we can calculate all the other system values,
such as the line flows and the generator reactive
power output

## Slide 18: Two Bus Case Low Voltage Solution

## Slide 19: Low Voltage Solution, cont'd
Low voltage solution

## Slide 20: Two Bus Region of Convergence
Slide shows the region of convergence for different initial
guesses of bus 2 angle (x-axis) and magnitude (y-axis)
Red region
converges
to the high
voltage
solution,
while the
yellow region
converges
to the low
voltage
solution

## Slide 21: August 14, 2003 Day Ahead Power Flow Low Voltage Solution Contour
The day ahead model had 65 energized 115,138, or 230 kV buses with voltages below 0.90 pu
The lowest 138 kV voltage was 0.836 pu; lowest 34.5 kV was 0.621 pu; case contained 42,766 buses; case had been used daily all summer

## Slide 22: PV Buses
Since the voltage magnitude at PV buses is fixed there is no need to explicitly include these voltages in x or write the reactive power balance equations
  the reactive power output of the generator varies to maintain the fixed terminal voltage (within limits)
  optionally these variations/equations can be included by just writing the explicit voltage constraint for the generator bus |Vi | – Vi setpoint = 0

## Slide 23: Three Bus PV Case Example

## Slide 24: Generator Reactive Power Limits
The reactive power output of generators varies to maintain the terminal voltage; on a real generator this is done by the exciter
To maintain higher voltages requires more reactive power
Generators have reactive power limits, which are dependent upon the generator's MW output
These limits must be considered during the power flow solution
These limits will be discussed further with the Newton-Raphson algorithm

## Slide 25: Generator Reactive Limits, cont'd
During power flow once a solution is obtained check to make generator reactive power output is within its limits
If the reactive power is outside of the limits, fix Q at the max or min value, and resolve treating the generator as a PQ bus
  this is know as "type-switching"
  also need to check if a PQ generator can again regulate
Rule of thumb: to raise system voltage we need to supply more vars

## Slide 26
400 MVA
15 kV
400 MVA
15/345 kV
T1
T2
800 MVA
345/15 kV
800 MVA
15 kV
520 MVA
80 MW
40 Mvar
280 Mvar
800 MW
Line 3 345 kV
Line 2
Line 1
345 kV 100 mi
345 kV 200 mi
50 mi
1
4
3
2
5
Single-line diagram
The N-R Power Flow: 5-bus Example
25

## Slide 27
Bus | Type | V per unit |  degrees | PG per unit | QG per unit | PL per unit | QL per unit | QGmax per unit | QGmin per unit
1 | Swing | 1.0 | 0 |  |  | 0 | 0 |  | 
2 | Load |  |  | 0 | 0 | 8.0 | 2.8 |  | 
3 | Constant voltage | 1.05 |  | 5.2 |  | 0.8 | 0.4 | 4.0 | -2.8
4 | Load |  |  | 0 | 0 | 0 | 0 |  | 
5 | Load |  |  | 0 | 0 | 0 | 0 |  | 
Table 1.
Bus input
data
Bus-to-Bus | R’ per unit | X’ per unit | G’ per unit | B’ per unit | Maximum MVA per unit
2-4 | 0.0090 | 0.100 | 0 | 1.72 | 12.0
2-5 | 0.0045 | 0.050 | 0 | 0.88 | 12.0
4-5 | 0.00225 | 0.025 | 0 | 0.44 | 12.0
Table 2.
Line input data
The N-R Power Flow: 5-bus Example
26
Notes: 26

## Slide 28
Bus-to-Bus | R per unit | X per unit | Gc per unit | Bm per unit | Maximum MVA per unit | Maximum TAP Setting per unit
1-5 | 0.00150 | 0.02 | 0 | 0 | 6.0 | —
3-4 | 0.00075 | 0.01 | 0 | 0 | 10.0 | —
Table 3.
Transformer
input data
Bus | Input Data | Unknowns
1 | V1 = 1.0, 1 = 0 | P1, Q1
2 | P2 = PG2-PL2 = -8 Q2 = QG2-QL2 = -2.8 | V2, 2
3 | V3 = 1.05 P3 = PG3-PL3 = 4.4 | Q3, 3
4 | P4 = 0, Q4 = 0 | V4, 4
5 | P5 = 0, Q5 = 0 | V5, 5
Table 4. Input data
and unknowns
The N-R Power Flow: 5-bus Example
27
Notes: 27

## Slide 29
Time to Close the Hood: Let the Computer Do the Math! (Ybus Shown)
28
Notes: 28