## Slide 1: ECEN 460 Power System Operation and Control
Lecture 3: Power Grid History, Three-Phase
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Please read Chapters 1, 2, 4.1-4.6
HW 1 is 2.9, 22, 28, 43, 48; due Thursday 9/14
  Regular problems (not multiple choice)
Labs will start next week (Sept 11)

## Slide 3: My Favorite 8/14/2003 Blackout Cartoon!

## Slide 4: My Favorite Blackout Hoax Photo

## Slide 5: The Smart Grid
The term “Smart Grid” dates officially to the 2007 “Energy Independence and Security Act”, Title 13 (“Smart Grid”)
  Use of digital information and control techniques
  Dynamic grid optimization with cyber-security
  Deployment of distributed resources including
  Customer participation and smart appliances
  Integration of storage including PHEVs
  Development of interoperability standards

## Slide 6: Smart Grid Perceptions (Some of Us Like the Term “Smarter”)

## Slide 7: Renewable Portfolio Standards (September 2012)
Source: http://www.dsireusa.org/

## Slide 8: Growth in Solar PV
Source: www.eia.gov/electricity/monthly/update/
We already covered the growth in wind

## Slide 9: Slowing Electric Load Growth
The total retail electric sales in 2013 were higher than in 2016
Source: EIA electric power monthly, August 2017

## Slide 10: Except in Texas!
Image source: CEO Perspectives, Bill Magness, ERCOT, May 2017

## Slide 11: In the News: Symantec Reports Hackers Have Access to US Grid
Electric companies have been targeted by hackers for many years. However, a new attack, by a group Symantec calls Dragonfly, seems to indicate some have possibly gained more operational access to grid systems in the US and Europe
They seek to get access to utility employee credentials through malicious emails and watering hole attacks (compromising websites used by power engineers)
Others cast doubt indicating hackers are far from being able to turn off the lights
Sources: www.businessinsider.com/symantec-hackers-sabotage-power-grid-2017-9, www.symantec.com/connect/blogs/dragonfly-western-energy-sector-targeted-sophisticated-attack-group

## Slide 12: Modeling Cautions!
"All models are wrong but some are useful," George Box, Empirical Model-Building and Response Surfaces, (1987, p. 424)
  Models are an approximation to reality, not reality, so they always have some degree of approximation
  Box went on to say that the practical question is how wrong to they have to be to not be useful
A good part of engineering is deciding what is the appropriate level of modeling, and knowing under what conditions the model will fail
Always keep in mind what problem you are trying to solve!

## Slide 13: Balanced Three-Phase () Systems
A balanced three-phase () system has
  three voltage sources with equal magnitude, but with an angle shift of 120
  equal loads on each phase
  equal impedance on the lines connecting the generators to the loads
Bulk power systems are almost exclusively 3
Single-phase is used primarily only in low voltage, low power settings, such as residential and some commercial

## Slide 14: Balanced 3 -- No Neutral Current

## Slide 15: Advantages of Three-Phase Power
Can transmit more power for same amount of wire (twice as much as single phase)
Torque produced by three-phase machines is constant
Three-phase machines use less material for same power rating
Three-phase machines start more easily than single-phase machines

## Slide 16: Three-Phase Wye Connection
There are two ways to connect 3 systems
  Wye (Y)
  Delta ()

## Slide 17: Wye Connection Line Voltages
Van
Vcn
Vbn
Vab
Vca
Vbc
-Vbn
Line to line
voltages are
also balanced
(α = 0 in this case)

## Slide 18: Wye Connection, cont’d
Define voltage/current across/through device to be phase voltage/current
Define voltage/current across/through lines to be line voltage/current

## Slide 19: Delta Connection
Ica
Ic
Iab
Ibc
Ia
Ib

## Slide 20: Three-Phase Example
Assume a -connected load is supplied from a 3 13.8 kV (L-L) source with Z = 10020W

## Slide 21: Three-Phase Example, cont’d

## Slide 22: Delta-Wye Transformation

## Slide 23: Delta-Wye Transformation Proof

## Slide 24: Delta-Wye Transformation, cont’d

## Slide 25: Three-Phase Transmission Line

## Slide 26: Per Phase Analysis
Per phase analysis allows analysis of balanced 3 systems with the same effort as for a single phase system
Balanced 3 Theorem: For a balanced 3 system with
  All loads and sources Y connected
  No mutual Inductance between phases

## Slide 27: Per Phase Analysis, cont’d
Then
  All neutrals are at the same potential
  All phases are COMPLETELY decoupled
  All system values are the same sequence as sources. The sequence order we’ve been using (phase b lags phase a and phase c lags phase a) is known as “positive” sequence (negative and zero sequence systems are mostly covered in ECEN 459)

## Slide 28: Per Phase Analysis Procedure
To do per phase analysis
Convert all  load/sources to equivalent Y’s
Solve phase “a” independent of the other phases
Total system power S = 3 Va Ia*
If desired, phase “b” and “c” values can be determined by inspection (i.e., ±120° degree phase shifts)
If necessary, go back to original circuit to determine line-line values or internal  values.

## Slide 29: Per Phase Example
Assume a 3, Y-connected generator with Van = 10 volts supplies a -connected load with Z = -j through a transmission line with impedance of j0.1 per phase. The load is also connected to a -connected generator with Va”b” = 10 through a second transmission line which also has an impedance of j0.1 per phase.
Find
1. The load voltage Va’b’
2. The total power supplied by each generator, SY and S

## Slide 30: Per Phase Example, cont’d

## Slide 31: Per Phase Example, cont’d

## Slide 32: Per Phase Example, cont’d

## Slide 33: Per Phase Example, cont’d

## Slide 34: Power System Operations Overview
Goal is to provide an intuitive feel for power system operation
Emphasis will be on the impact of the transmission system
Introduce basic power flow concepts through small system examples

## Slide 35: Power System Operations Overview
Goal is to provide an intuitive feel for power system operation
Emphasis will be on the impact of the transmission system
Introduce basic power flow concepts through small system examples

## Slide 36: Power System Basics

## Slide 37: Electric Loads
Can range in size from less than one watt to 10’s of MW
Load are usually aggregated.
The aggregate load changes with time, with strong daily, weekly and seasonal cycles.

## Slide 38: Electric Load Yearly Variation
Data source: FERC 714 filings, 2004

## Slide 39: Example: PJM Weekly Summer Load Variation, July 2013

## Slide 40: Example: PJM Weekly Winter Load Variation, February 2015

## Slide 41: Example: Daily Variation for CA