## Slide 1: ECEN 615 Methods of Electric Power Systems Analysis
Lecture 8: Sparse Systems
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Read Chapter 6 from the book
  The book presents the power flow using the polar form for the Ybus elements
Homework 2 is due on Thursday September 22
The ECEN EPG dinner is Saturday October 1st at 5:00 pm at Prof. Davis’s house. The address is 3810 Park Meadow Lane, Bryan, TX 77802.
  RSVP at https://forms.gle/6aye2butgCLDv6bz5 by Sunday, September 25th.

## Slide 3: Homework comments
You can program in the language of your choice
An open source alternative to Matlab is Scilab (scilab.org)
One approach to developing code is to start small, get it working, then expand (start with solving a two bus power flow)
A singular Jacobian indicates too many unknowns. For example, with a two bus, one line dc power flow with z = j0.1 and bus 1 the slack, then

## Slide 4: LU Algorithm Without Pivoting Processing by row
We will use the more common approach of having ones on the diagonals of L. Also in the common, diagonally dominant power system problems pivoting is not needed. The below algorithm is in row form (useful with sparsity!)
For i := 2 to n Do Begin // This is the row being processed
For j := 1 to i-1 Do Begin // Rows subtracted from row i
A[i,j] = A[i,j]/A[j,j] // This is the scaling
For k := j+1 to n Do Begin // Go through each column in i
A[i,k] = A[i,k] - A[i,j]*A[j,k]
End;
End;
End;

## Slide 5: Forward Substitution
Forward substitution solves with values in b being over written (replaced by the y values) For i := 2 to n Do Begin // This is the row being processed
For j := 1 to i-1 Do Begin
b[i] = b[i] - A[i,j]*b[j] // This is just using the L matrix
End;
End;

## Slide 6: Backward Substitution
Backward substitution solves (with values of y contained in the b vector as a result of the forward substitution)
For i := n to 1 Do Begin // This is the row being processed
For j := i+1 to n Do Begin
b[i] = b[i] - A[i,j]*b[j] // This is just using the U matrix
End;
b[i] = b[i]/A[i,i] // The A[i,i] values are <> 0 if it is nonsingular
End

## Slide 7: Computational Complexity
Computational complexity indicates how the number of numerical operations scales with the size of the problem
Computational complexity is expressed using the “Big O” notation; assume a problem of size n
  Adding the number of elements in a vector is O(n)
  Adding two n by n full matrices is O(n2)
  Multiplying two n by n full matrices is O(n3)
  Inverting an n by n full matrix, or doing Gaussian elimination is O(n3)
  Solving the traveling salesman problem by brute-force search is O(n!)

## Slide 8: Computational Complexity
Knowing the computational complexity of a problem can help to determine whether it can be solved (at least using a particular method)
  Scaling factors do not affect the computation complexity
    an algorithm that takes n3/2 operations has the same computational complexity of one the takes n3/10 operations (though obviously the second one is faster!)
With O(n3) factoring a full matrix becomes computationally intractable quickly!
  A 100 by 100 matrix takes a million operations (give or take)
  A 1000 by 1000 matrix takes a billion operations
  A 10,000 by 10,000 matrix takes a trillion operations!

## Slide 9: Sparse Systems
The material presented so far applies to any arbitrary linear system
The next step is to see what happens when we apply triangular factorization to a sparse matrix
For a sparse system, only nonzero elements need to be stored in the computer since no arithmetic operations are performed on the 0’s
The LU factorization is adapted to solve sparse systems in such a way as to preserve the sparsity as much as possible

## Slide 10: Sparse Matrix History
A nice overview of sparse matrix history is by Iain Duff at http://www.siam.org/meetings/la09/talks/duff.pdf
Sparse matrices developed simultaneously in several different disciplines in the early 1960’s with power systems definitely one of the key players (Bill Tinney from BPA)
Different disciplines claim credit since they didn’t necessarily know what was going on in the others

## Slide 11: Sparse Matrix History
  In power systems a key N. Sato, W.F. Tinney, “Techniques for Exploiting the Sparsity of the Network Admittance Matrix,” Power App. and Syst., pp 944-950, December 1963
    In the paper they are proposing solving systems with up to 1000 buses (nodes) in 32K of memory!
    You’ll also note that in the discussion by El-Abiad, Watson, and Stagg they mention the creation of standard test systems with between 30 and 229 buses (this surely included the now famous 118 bus system)
    The BPA authors say “power flow” and the discussors say “load flow.”
  Tinney and Walker present a much more detailed approach in their 1967 IEEE Proceedings paper titled “Direct Solutions of Sparse Network Equations by Optimally Order Triangular Factorization”

## Slide 12: Sparse Matrix Computational Order
The computational order of factoring a sparse matrix, or doing a forward/backward substitution depends on the matrix structure
  Full matrix is O(n3)
  A diagonal matrix is O(n); that is, just invert each element
For power system problems the classic paper is F. L. Alvarado, “Computational complexity in power systems,” IEEE Transactions on Power Apparatus and Systems, ,May/June 1976
  O(n1.4) for factoring, O(n1.2) for forward/backward
  For a 100,000 by 100,000 matrix changes computation for factoring from 1 quadrillion to 10 million!
  Updated statistics are given in F. Safdarian, Z. Mao, W. Jang, and T. J. Overbye, “Power System Sparse Matrix Statistics,” IEEE Texas Power and Energy Conference, College Station, TX, February 2022

## Slide 13: Inverse of a Sparse Matrix
The inverse of a sparse matrix is NOT in general a sparse matrix
We never (or at least very, very, very seldom) explicitly invert a sparse matrix
  Individual columns of the inverse of a sparse matrix can be obtained by solving x = A-1b with b set to all zeros except for a single nonzero in the position of the desired column
  If a few desired elements of A-1 are desired (such as the diagonal values) they can usually be computed quite efficiently using sparse vector methods (a topic we’ll be considering soon)
We can’t invert a singular matrix (whether sparse or full)

## Slide 14: Computer Architecture Impacts
With modern computers the processor speed is many times faster than the time it takes to access data in main memory
  Some instructions can be processed in parallel
Caches are used to provide quicker access to more commonly used data
  Caches are smaller than main memory
  Different cache levels are used with the quicker caches, like L1, have faster speeds but smaller sizes; L1 might be 256K, whereas the slower L2 might be 2M
Data structures can have a significant impact on sparse matrix computation

## Slide 15: Full Matrix versus Sparse Matrix Storage
Full matrices are easily stored in arrays with just one variable needed to store each value since the value’s row and column are implicitly available from its matrix position
With sparse matrices two or three elements are needed to store each value
  The zero values are not explicitly stored
  The value itself, its row number and its column number
  Storage can be reduced by storing all the elements in a particular row or column together
Because large matrices are often quite sparse, the total storage is still substantially reduced

## Slide 16: Sparse Matrix Usage Can Determine the Optimal Storage
How a sparse matrix is used can determine the best storage scheme to use
  Row versus column access; does the structure change
Is the matrix essentially used only once? That is, its structure and values are assumed new each time used
Is the matrix structure constant, with its values changed
  This would be common in the N-R power flow, in which the structure doesn’t change each iteration, but its values do
Is the matrix structure and values constant, with just the b vector in Ax=b changing
  Quite common in power system stability solutions

## Slide 17: Numerical Precision
Required numerical precision determines type of variables used to represent numbers
  Specified as number of bytes, and whether signed or not
For Integers
  One byte is either 0 to 255 or -128 to 127
  Two bytes is either smallint (-32,768 to 32,767) or word (0 to 65,536)
  Four bytes is either Integer (-2,147,483,648 to 2,147,483,647) or Cardinal (0 to 4,294,967,295)
    This is usually sufficient for power system row/column numbers
  Eight bytes (Int64) if four bytes is not enough

## Slide 18: Numerical Precision, cont.
For floating point values using choice is between four bytes (single precision) or eight bytes (double precision); extended precision has ten bytes
  Single precision allows for 6 to 7 significant digits
  Double precision allows for 15 to 17 significant digits
  Extended allows for about 18 significant digits
  More bytes requires more storage
  Computational impacts depend on the underlying device; on PCs there isn’t much impact; GPUs can be 3 to 8 times slower for double precision
For most power problems double precision is best

## Slide 19: General Sparse Matrix Storage
A general approach for storing a sparse matrix would be using three vectors, each dimensioned to number of elements
      AA: Stores the values, usually in power system analysis as double precision values (8 bytes)
      JR: Stores the row number; for power problems usually as an integer (4 bytes)
      JC: Stores the column number, again as an integer
    If unsorted then both row and column are needed
    New elements could easily be added, but costly to delete
    Unordered approach doesn’t make for good computation since elements used next computationally aren’t necessarily nearby
    Usually ordered, either by row or column

## Slide 20: Sparse Storage Example
Assume
Then
Note, this example is a symmetric matrix, but the technique is general

## Slide 21: Compressed Sparse Row Storage
If elements are ordered (as was case for previous example) storage can be further reduced by noting we do not need to continually store each row number
A common method for storing sparse matrices is known as the Compressed Sparse Row (CSR) format
  Values are stored row by row
  Has three vector arrays:
    AA: Stores the values as before
    JA: Stores the column index (done by JC in previous example)
    IA: Stores the pointer to the index of the beginning of each row
20

## Slide 22: CSR Format Example
Assume as before
Then
21

## Slide 23: CSR Comments
The CSR format reduces the storage requirements by taking advantage of needing only one element per row
The CSR format has good advantages for computation when using cache since (as we shall see) during matrix operations we are often sequentially going through the vectors
An alternative approach is Compressed Sparse Column (CSC), which identical, except storing the values by column
It is difficult to add values.
We’ll mostly use the linked list approach here, which makes matrix manipulation simpler
22

## Slide 24: Linked Lists: Classes and Objects
In explaining the linked list approach it is helpful to use the concepts from object oriented programming (OOP) of classes and objects
  Approach can also be used in non-OOP programming
OOP can be thought of as a collection of objects interacting with each other
Objects are instances of classes.
Classes define the object fields and actions (methods)
We’ll define a class called sparse matrix element, with fields of value, column and next; each sparse matrix element is then an object of this class
23

## Slide 25: Linked Lists
A linked list is just a group of objects that represent a sequence
  We’ll used linked lists to represent a row or column of a sparse matrix
Each linked list has a head pointer that points to the first object in the list
  For our sparse matrices the head pointer will be a vector of the rows or columns
Column a
Value a
Next a
Column b
Value b
Next b
Column c
Value c
Nil
Head
24

## Slide 26: Sparse Matrix Storage with Linked Lists by Rows
If we have an n by n matrix, setup a class called TSparseElement with fields column, value and next
Setup an n-dimensional head pointer vector that points to the first element in each row
Each nonzero corresponds to an object of class (type) TSparseElement
We do not need to store the row number since it is given by the object’s row
For power system sparse matrices, which have nonzero diagonals, we also have a header pointer vector that points to the diagonal objects
25

## Slide 27: Linked Lists, cont.
Linked lists can be singly linked, which means they just go in one direction (to the next element), or doubly linked, pointing to both the previous and next elements
  Mostly we’ll just need singularly linked lists
With linked lists it is quite easy to add new elements to the list. This can be done in sorted order just by going down the list until the desired point is reached, then changing the next pointer for the previous element to the new element, and for the new element to the next element (for a singly linked list)
26

## Slide 28: Example Pascal Code for Writing a Sparse Matrix
Procedure TSparMat.SMWriteMatlab(Var ft : Text; variableName : String; digits,rod : Integer; ignoreZero : Boolean; local_MinValue : Double);
Var j : Integer;
p1 : TMatEle;
Begin
For j := 1 to n Do Begin
p1 := Row(j).Head;
While p1 <> nil Do Begin
If (not IgnoreZero) or (abs(p1.value) > local_MinValue) Then Begin
If variableName <> '' Then Writeln(ft,variableName+'(',(j),',',(p1.col),')=',p1.value:digits:rod,';')
Else Writeln(ft,j:5,' ',p1.col:5,' ',p1.value:digits:rod);
End;
p1 := p1.next;
End;
End;
End;
27

## Slide 29: Sparse Working Row
Before showing a sparse LU factorization it is useful to introduce the concept of a working row full vector
This is useful because sometimes we need direct access to a particular value in a row
The working row approach is to define a vector of dimension n and set all the values to zero
We can then load a sparse row into the vector, with computation equal to the number of elements in the row
We can then unload the sparse row from the vector by storing the new values in the linked list, and resetting the vector values we changed to zero
28

## Slide 30: Loading the Sparse Working Row
Procedure TSparMat.LoadSWRbyCol(rowJ : Integer; var SWR : PDVectorList);
Var p1 : TMatEle;
Begin
p1 := rowHead[rowJ];
While p1 <> nil Do Begin
SWR[p1.col] := p1.value;
p1 := p1.next;
End;
End;
29

## Slide 31: Unloading the Sparse Working Row
Procedure TSParMat.UnLoadSWRbyCol(rowJ : Integer; var SWR : PDVectorList);
Var p1 : TMatEle;
Begin
p1 := rowHead[rowJ];
While p1 <> nil Do Begin
p1.value := SWR[p1.col];
SWR[p1.col] := 0;
p1 := p1.next;
End;
End;
Note, there is no need to explicitly zero out all the elements each iteration since 1) most are still zero and 2) doing so would make it O(n2). The above code efficiently zeros out just the values that have changed.
30

## Slide 32: Doing an LU Factorization of a Sparse Matrix with Linked Lists
Now we can show how to do an LU factorization of a sparse matrix stored using linked lists
We will assume the head pointers are in the vector RowHead, and the diagonals in RowDiag
Recall this was the approach for the full matrix
For i := 2 to n Do Begin // This is the row being processed
For j := 1 to i-1 Do Begin // Rows subtracted from row i
A[i,j] = A[i,j]/A[j,j] // This is the scaling
For k := j+1 to n Do Begin // Go through each column in i
A[i,k] = A[i,k] - A[i,j]*A[j,k]
End;
End;
End;
31

## Slide 33: Sparse Factorization
Note, if you know about fills, we will get to that shortly; if you don’t know don’t worry about it yet
We’ll just be dealing with structurally symmetric matrices (incidence-symmetric)
We’ll assume the row linked lists are ordered by column; we’ll show how this can be done quickly later
We will again sequentially going through the rows, starting with row 2, going to row n For i := 2 to n Do Begin // This is the row being processed
32

## Slide 34: Sparse Factorization, cont.
The next step is to go down row i, up to but not including the diagonal element
We’ll be modifying the elements in row i, so we need to load them into the working row vector
Key sparsity insight is in doing the below code we only need to consider the non-zeros in A[i,j]; for a full matrix the code is For j := 1 to i-1 Do Begin // Rows subtracted from row A[i,j] = A[i,j]/A[j,j] // This is the scaling For k := j+1 to n Do Begin // Go through each column in i A[i,k] = A[i,k] - A[i,j]*A[j,k]
End;
33

## Slide 35: Sparse Factorization, cont.
For i := 1 to n Do Begin // Start at 1, but nothing to do in first row
LoadSWRbyCol(i,SWR); // Load Sparse Working Row }
p2 := rowHead[i]
While p2 <> rowDiag[i] Do Begin // This is doing the j loop
p1 := rowDiag[p2.col];
SWR[p2.col] := SWR[p2.col] / p1.value;
p1 := p1.next;
While p1 <> nil Do Begin // Go to the end of the row
SWR[p1.col] := SWR[p1.col] - SWR[p2.col] *p1.value;
p1 := p1.next;
End;
p2 := p2.next;
End;
UnloadSWRByCol(i,SWR);
End;
34

## Slide 36: Sparse Factorization Example
Believe it or not, that is all there is to it! The factorization code itself is quite simple.
However, there are a few issues we’ll get to in a second. But first an example
Notice with this example there is nothing to do with rows 1, 2 and 3 since there is nothing before the diag (p2 will be equal to the diag for the first three rows)
35

## Slide 37: Sparse Factorization Example, Cont.
Doing factorization with i=4
  Row 4 is full so initially p2= A[4,1] // column 1
  SWR = [-4 -3 -2 10]
  p1= A[1,1]
  SWR[1] = -4/A[1,1] = -4/5 = -0.8
  p1 goes to A[1,4]
  SWR[4] = 10 – SWR[p2.col]*p1.value = 10 – (-0.8)*-4=6.8
  p1 = nil; go to next col
  p2 =A[4,2] // column 2
  P1 = A[2,2]
  SWR[2] = -3/A[2,2]= -3/4 = -0.75
That is, the next element in row 1
36

## Slide 38: Sparse Factorization Example, Cont.
  p1 goes to A[2,4] // p2=A[4,2]
  SWR[4] = 6.8 – SWR[p2.col]*p1.value = 6.8 – (-0.75)*-3=4.55
  p1 = nil; go to next col
  p2 =A[4,3] // column 3
  p1 = A[3,3]
  SWR[3] = -/A[2,2]= -2/3 = -0.667
  p1 goes to A[3,4] // p2 = A[4,3]
  SWR[4] = 4.55 – SWR[p2.col]*p1.value = 4.55 – (-0.667)*-2=3.2167
  Unload the SWR = [-0.8 -0.75 -0.667 3.2167]
  p2 = A[4,4] = diag so done
The next element in row 2
The next element in row 3
37

## Slide 39: Sparse Factorization Examples, Cont.
For a second example, again consider the same system, except with the nodes renumbered
38

## Slide 40: Sparse Factorization Examples, Cont.
With i=2, load SWR = [-4 5 0 0]
  p2 = B[2,1]
  p1 = B[1,1]
  SWR[1]=-4/p1.value=-4/10 = -0.4
  p1 = B[1,2]
  SWR[2]=5 – (-0.4)*(-4) = 1.6
  p1 = B[1,3]
  SWR[3]= 0 – (-0.4)*(-3) = -1.2
  p1 = B[1,4]
  SWR[4]=0 – (-0.4)*(-2) = -0.8
  p2=p2.next=diag so done
  UnloadSWR and we have a problem!
There are no elements in row 2 for columns 3 and 4!
39

## Slide 41: Fills
When doing a factorization of a sparse matrix some values that were originally zero can become nonzero during the factorization process
These new values are called “fills” (some call them fill-ins)
For a structurally symmetric matrix the fill occurs for both the element and its transpose value (i.e., Aij and Aji)
How many fills are required depends on how the matrix is ordered
  For a power system case this depends on the bus ordering
40

## Slide 42: Fills
There are two key issues associated with fills
  Adding the fills
  Ordering the matrix elements (buses in our case) to reduce the number of fills
The amount of computation required to factor a sparse matrix depends upon the number of nonzeros in the original matrix, and the number of fills added
How the matrix is ordered can have a dramatic impact on the number of fills, and hence the required computation
Usually a matrix cannot be ordered to totally eliminate fills
41

## Slide 43: Fill Examples
4
1
2
3
1
2
3
4
No Fills Required
Fills Required (matrix becomes full)
42

## Slide 44
Example: 7 by 7 Matrix
Consider the 7 x 7 matrix A with the zero-nonzero pattern shown in (a): of the 49 possible elements there are only 31 that are nonzero
If elimination proceeds with the given ordering, all but two of the 18 originally zero entries, will fill in, as seen in (b)
43

## Slide 45
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | X | X | X | X | X | X | 
2 | X | X | X |  |  | X | X
3 | X | X | X |  |  | X | X
4 | X |  |  | X | X |  | 
5 | X |  |  | X | X | X | 
6 | X | X | X |  | X | X | 
7 |  | X | X |  |  |  | X
  The original zero-nonzero structure
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | X | X | X | X | X | X | 
2 | X | X | X | F | F | X | X
3 | X | X | X | F | F | X | X
4 | X | F | F | X | X | F | F
5 | X | F | F | X | X | X | F
6 | X | X | X | F | X | X | F
7 |  | X | X | F | F | F | X
The post- elimination zero nonzero pattern
r
c
r
c
Example: 7 by 7 Matrix Structure
44

## Slide 46
We next reorder the rows and the columns of A so as to result in the pattern shown in (c)
For this reordering, we obtain no fills, as shown in the table of factors given in (d )
In this way, we preserve the original sparsity of A
Example: 7 by 7 Matrix Reordering
45

## Slide 47
 | 4 | 5 | 1 | 6 | 7 | 3 | 2
4 | X | X | X |  |  |  | 
5 | X | X | X | X |  |  | 
1 | X | X | X | X |  | X | X
6 |  | X | X | X |  | X | X
7 |  |  |  |  | X | X | X
3 |  |  | X | X | X | X | X
2 |  |  | X | X | X | X | X
The reordered system
 | 4 | 5 | 1 | 6 | 7 | 3 | 2
4 | X | X | X |  |  |  | 
5 | X | X | X | X |  |  | 
1 | X | X | X | X |  | X | X
6 |  | X | X | X |  | X | X
7 |  |  |  |  | X | X | X
3 |  |  | X | X | X | X | X
2 |  |  | X | X | X | X | X
The post- elimination reordered system
r
c
r
c
Example: 7 by 7 Matrix Reordered Structure
46

## Slide 48
For electric grids it can be helpful to relate the sparse matrix back to an associated electric grid
Assume an n by n matrix A
All the diagonals are non-zeros
If there is a connection between two buses (nodes), say at position j and k, then the associated matrix entries, Ajk and Akj are nonzero
Graph (Grid) Insights
47