## Slide 1: ECEN 460 Power System Operation and Control Spring 2025
Lecture 24: Wind and Solar
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
Texas A&M University
overbye@tamu.edu

## Slide 2: Announcements
Please read Chapter 13
Schedule for the rest of the semester is
  No labs this Friday (Reading Day)
  Lab 11 (project presentations) by the individual teams to their TA ideally before the end of classes (on or before April 29)
  Exam 2 on Wednesday April 23 during class; comprehensive but more emphasis on material since the first exam; similar format to first exam, closed book, closed notes, but two 8.5 by 11 inch note sheets and calculators allowed
  Design project due at 9:30 am on May 1 (i.e., at the end of our final slot; no final)
1

## Slide 3: Renewable Resource Introduction and Modeling
With the advent of more renewable generation in power systems worldwide it is important to have correct models
Hydro systems have already been covered
Solar thermal and geothermal are modeled similar to existing stream generation, so they are not covered here
Coverage will focus on introducing wind and solar generation, along with their associated power flow and stability level models for wind and solar PV for integrated system studies
  More detailed EMTP-level models may be needed for individual plant issues, like subsynchronous resonance
  Models are evolving, with a desire by many to have as generic as possible models
2

## Slide 4: Inverter-Based Resources (IBRs)
The term inverter-based resources (IBRs) is used to refer to devices that connect to the power grid through an inverter
  An inverter is a device that takes a dc input and converts it to ac at a specified frequency; a rectifier is the inverse of an inverter, dc to ac
Inverters can produce or absorb reactive power, providing great flexibility; however, they are limited by their power rating
IBRs are now widely used in the power grid to connect in wind turbines, solar photovoltaic arrays (pv), storage, and HVDC
A short document describing IBRs is available from NERC at
  www.nerc.com/pa/Documents/2023_NERC_Guide_Inverter-Based-Resources.pdf
3

## Slide 5: Differences between IBRs and Synchronous Generators
  Images from www.nerc.com/pa/Documents/2023_NERC_Guide_Inverter-Based-Resources.pdf
4

## Slide 6: Changing Sources of Generation
In the US and worldwide the sources of electricity are rapidly changing
5

## Slide 7: Changing Sources of Generation, cont.
The sources variety substantially by state, the below image shows the change in the ERCOT (Texas) generation
6

## Slide 8: Natural Gas Prices, A Key Driver of Electricity Prices
Source: fred.stlouisfed.org/series/DHHNGSP
7

## Slide 9: Planned New Generation 2025
Two 1100 MW nuclear units, Vogtle 3 and 4, entered commercial operation on 2023 and 2024 respectively; Texas is expected to add 6.7 GW of new storage in 2025
8
Vineyard Wind 1 is under construction and might enter operation in 2025; Revolution Wind might go into operation in 2026

## Slide 10: US Wind and Solar Capacity by State, 2024
Total US capacity at the end of Q4 2024 is about 155 GW of wind, 130 GW of solar, and 29 GW of storage (compared to a total US generation capacity of about 1300 GW)
9

## Slide 11: US Annual & Cumulative Wind & Solar Growth
Source: American Clean Power Quarterly, 2024 Q4
10

## Slide 12: North America Wind Resources at 100 m
11
Source: www.nrel.gov/docs/fy15osti/64733.pdf
Wind speeds at say 100 m above the ground can be substantially higher than closer to the surface; above 7.5 m/s is economic

## Slide 13: US Wind Farm Locations, Feb 2025
Image source: USGS at https://eerscmap.usgs.gov/uswtdb/
12
Many wind turbines are usually sited together, in groups known as either wind farms, wind parks, or wind power plants; single devices are known as wind turbines, with the term windmill usually used for devices that pump water

## Slide 14: Wind Map Texas– 80m Height
https://windexchange.energy.gov/files/u/visualization/image/tx_80m.jpg
13
Wind farms in Texas

## Slide 15: Power in the Wind
The power in the wind is proportional to the cube of the wind speed
  Velocity increases with height, with more increase over rougher terrain (doubling at 100m compared to 10m for a small town, but only increasing by 60% over crops or 30% over calm water)
Maximum rotor efficiency is 59.3%, from Betz' law
Expected available energy depends on the wind speed probability density function (pdf)
14

## Slide 16: Determining Available Wind Energy
Because the power in the wind varies with the cube of the wind speed, just knowing the average wind speed is not sufficient to determine the available wind energy; the wind speed probability distribution function (pdf) is also needed
When the actual wind pdf is not available, it is common to assume a Rayleigh pdf, which is a Weibull pdf with a k = 2
For Rayleigh
15

## Slide 17: Wind Turbine Height and Size
The current largest wind turbines by capacity are about 26 MW with rotor diameters of about 340m; the below picture is for an 18 MW generator
Average on-shore capacities are now over 3 MW, with hub heights approaching 100 m
https://www.energy.gov/eere/articles/wind-turbines-bigger-better
16

## Slide 18: Extracted Power
WTGs are designed for rated power and windspeed
  For speeds above this blades are pitched to operate at rated power; at furling speed the WTG is cut out
17

## Slide 19: Example: GE 1.5 and 1.6 MW Turbines
Power speed curves for the GE 1.5 and 1.6 MW WTGs
  Hub height is 80/100 m; cut-out at 25 m/s wind
Source: http://site.ge-energy.com/prod_serv/products/wind_turbines/en/15mw/index.htm
18

## Slide 20: Wind Farms (or Parks)
Usually, wind farm is modeled in aggregate for grid studies; wind farm can consist of many small (1 to 3 MW) wind turbine-generators (WTGs) operating at low voltage (e.g. 0.6kV) stepped up to distribution level (e.g., 34.5 kV)
Photo Source: www.energyindustryphotos.com/photos_of_wind_farm_turbines.htm
19

## Slide 21: Economies of Scale
Presently large wind farms produce electricity more economically than small operations
Factors that contribute to lower costs are
  Wind power is proportional to the area covered by the blade (square of diameter) while tower costs vary with a value less than the square of the diameter
  Larger blades are higher, permitting access to faster winds, but size limited by transportation for most land wind farms
  Fixed costs associated with construction (permitting, management) are spread over more MWs of capacity
  Efficiencies in managing larger wind farms typically result in lower O&M costs (on-site staff reduces travel costs)
20

## Slide 22: Wind Patterns
Wind speeds, of course, vary. However, they usually exhibit daily and seasonal patterns that the be leveraged in electric grid planning and operation; the below images show data for ERCOT locations, both daily and monthly
Images: www.ercot.com/files/docs/2017/02/17/MemoReport_AWST_ERCOT_27Mar2015.pdf
21

## Slide 23: Offshore Wind
Offshore wind turbines currently need to be in relatively shallow water, so maximum distance from shore depends on the seabed
Worldwide capacity is about 70 GW, with half of it in China and almost one quarter in the UK
  US offshore wind is only 42 MW; while there had been lots of interest, there are also major challenges including greatly increased costs
Capacity factors tend to increase as turbines move further off-shore
Image Source: National Renewable Energy Laboratory
22

## Slide 24: Offshore: Advantages and Disadvantages
All advantages/disadvantages are somewhat site specific
Advantages
  Can usually be sited much closer to the load (which is often by the coasts)
  Offshore wind speeds are higher and steadier
  Easier to transport large wind turbines by ship
  Minimal sound impacts and visual impacts (if far enough offshore), no land usage issues
Disadvantages
  High construction costs, particularly since they are in windy (and hence wavy) locations
  Higher maintenance costs
  Some environmental issues (e.g., seabed disturbance)
23

## Slide 25: Types of Wind Turbines for Power Flow and Stability
Several different approaches to aggregate modeling of wind farms in power flow and transient stability
  Wind turbine manufacturers provide detailed, public models of their WTGs; these models are incorporated into software packages; for example, GE 1.5, 1.6 and 3.6 MW WTGs (see Modeling of GE Wind Turbine-Generators for Grid Studies, version 6.01, October 2017, GE Energy)
  Proprietary models are included as user defined models; covered under NDAs to maintain confidentiality
  Generic models are developed to cover the range of WTGs, with parameters set based on the individual turbine types
    Concern by some manufacturers that the generic models to not capture their WTGs' behavior, such as during low voltage ride through (LVRT)
24

## Slide 26: Types of Wind Turbines for Power Flow and Stability
Electrically there are four main generic types of wind turbines
  Type 1: Induction machine; treated as PQ bus with negative P load; dynamically modeled as an induction motor
  Type 2: Induction machine with varying rotor resistance; treated as PQ bus in power flow; induction motor model with dynamic slip adjustment
  Type 3: Doubly Fed Asynchronous Generator (DFAG) (or DFIG); treated as PV bus in power flow
  Type 4: Full Asynchronous Generator; treated as PV bus in power flow
New wind farms (or parks) are all of Type 3 or 4
25

## Slide 27: Generic Modeling Approach
The generic modeling approach is to divide the wind farm models by functionality
  Generator model: either an induction machine for Type 1 and 2's or a voltage source converter for Type 3 and 4
  Reactive power control (exciter): none for Type 1, rotor resistance control for Type 2, commanded reactive current for Type 3 and 4
  Drive train models: Type 1 and 2 in which the inertia appears in the transient stability
  Aerodynamics and Pitch Models: Model impact of changing blade angles (pitch) on power output
26

## Slide 28: Wind Turbine Issues
Models are designed to represent the system level impacts of the aggregate wind turbines during disturbances such as low voltages (nearby faults) and frequency deviations
Low voltage ride through (LVRT) is a key issue, in which the wind turbines need to stay connected to the grid during nearby faults
Active and reactive power control is also an issue
27

## Slide 29: Low Voltage Ride Through (LVRT)
The concern is if during low voltages, such as during faults, the IBRs trip, it could quickly setup a cascading situation particularly in areas with lots of wind, solar or storage
  For WTGs rapid tripping had been a strategy to protect the DFAG from high rotor currents and over voltages in the dc capacitor.
  When there were just a few WTGs, tripping was acceptable
Different interconnects have varying requirements, with ERCOT having a more restrictive
28
Image source: ERCOT, 2023

## Slide 30: Type 3: Doubly Fed Asynchronous Generators (DFAG)
Doubly fed asynchronous generators (DFAG) are usually a conventional wound rotor induction generator with an ac-dc-ac power converter in the rotor circuit
  Power that would have been lost in external rotor resistance is now used
Electrical dynamics are dominated by the voltage- source inverter, which has dynamics much faster than the transient stability time frame
Image Source: Figure 2.1 from Modeling of GE Wind Turbine-Generators for Grid Studies, version 4.6, March 2013, GE Energy
29

## Slide 31: Type 3 Converters
A voltage source converter (VSC) takes a dc voltage, usually held constant by a capacitor, and produces a controlled ac output
A phase locked loop (PLL) is used to synchronize the phase of the wind turbine with that of the ac connection voltage
  Operates much faster than the transient stability time step, so is often assumed to be in constant synchronism
Under normal conditions the WTG has a controllable real power current and reactive power current
WTG voltages are not particularly high, say 600V
30

## Slide 32: Type 3 Converters
Type 3 machines can operate at a potentially widely varying slip
  Example, rated speed might be 120% (72 Hz for a 60 Hz system) with a slip of -0.2, but with a control range of +/- 30%
Control systems are used to limit the real power during faults (low voltage)
  Current ramp rate limits are used to prevent system stress during current recovery
Reactive current limits are used during high voltage conditions
31

## Slide 33: Type 4 Converters
Type 4 WTGs pass the entire output of the WTG through the ac-dc-ac converter
Hence the system characteristics are essentially independent of the type of generator
  Because of this decoupling, the generator speed can be as variable as needed
  This allows for different generator technologies, such as permanent magnet synchronous generators (PMSGs)
  Traditionally gearboxes have been used to change the slow wind turbine speed (e.g., 15 rpm) to a more standard generator speed (e.g., 1800 rpm); with Type 4 direct drive technologies can also be used
32

## Slide 34: Stability Modeling of Wind Turbines
As we’ve seen, traditionally the industry has used a modular approach for generator models
  Machine
  Exciter
  Governor
  Stabilizer
  Under Excitation Limiter
  Over Excitation Limiter
  Relay Models
  Compensator Model
33

## Slide 35: This Approach Has Been Followed with Wind
When wind started to appear in larger amounts, “first generation” models were developed following this same approach
This initial models were a good start, but they are now considered obsolete
First Generation model had few mechanisms to provide control features of
  Real Power or Torque Control
  Reactive Power
  Voltage Control
34

## Slide 36: Second Generation Stability Models
The second generation models are a similar format, but provide for more realistic control; they have also been expanded to include solar and storage
Second Generation Type 3 Models
35

## Slide 37: 2nd Generation Type 3 Wind Turbine (REGC_A, REEC_A, WTGT_A, WTGAR_A, WTGPT_A, WTGTRQ_A, REPC_A)
Exciter REEC_A
Machine REGC_A
Voltage Compensation
Stabilizer WTGPT_A
Governor WTGT_A
PRef Controller WTGTRQ_A
Plant Level Controller REPC_A
wg
wt
ϴ
Aero WTGAR_A
Pm
ωref
Qref/Vref
Pref
Vcomp
Ipord
Pref0
Iq
Ip
Pord
Network
Iqord
2nd Generation adds the Aero, PRef and Plant Controllers
36

## Slide 38: 2nd Generation Type 4 Wind Turbine (REGC_A, REEC_A, WTGT_A, REPC_A)
Exciter REEC_A
Machine REGC_A
Voltage Compensation
Network
Governor WTGT_A
Plant Level Controller REPC_A
wg
Tm0
Qref/Vref
Pref
Vcomp
Ipord
Iq
Ip
Iqord
Note: If REEC_A parameter Pflag = 0, then WTGT_A really doesn’t do anything so it can be omitted completely
37

## Slide 39
Inputs from
REEC* electrical models
“Machine Model”: really a network interface
38
Second Generation “Machine” Model, REGC_A (or REGCA1)

## Slide 40: REEC_A (same as REECA1)
Outputs
REGC* machine model
Outputs
REGC* machine model
Pref Input from
REPC* Plant Controller WTGTRQ* Pref Controller
Qext Input from
REPC* Plant Controller
wg Input from
WTGT* mechanical
Electrical Model
39

## Slide 41: Additional Wind Farm Issues
Wind turbines certainly kill birds and bats, but so do lots of other things; however, wind turbines can kill the longer-lived, larger birds such as raptors that can be especially sensitive to adult mortabilites
40

## Slide 42: Additional Wind Farm Issues, cont.
Wind turbines can enhance the well-being of many people (e.g., financially), but some living nearby may be affected by noise and shadow flicker
Noise comes from 1) the gearbox/generator and 2) the aerodynamic interaction of the blades with the wind
Noise impact is usually moderate (50-60 dB) close (40m), and lower further away (35-45 dB) at 300m
  However, wind turbine frequencies also need to be considered, with both a “hum” frequency above 100 Hz, and some barely audible low frequencies (20 Hz or less)
Shadow flicker is more of an issue in high latitude countries since a lower sun casts longer shadows
Night lighting and aesthetics in general can be concerns
41

## Slide 43: Example Noise and Shadow Flicker Maps
Left source: www.sciencedirect.com/science/article/pii/S2214629621005582; right source: https://netzeroatlantic.ca/hub/wind/onshore
With noise, 40-50 dB is refrigerator or quiet office; however, low frequencies can be a concern for some people
42

## Slide 44: Solar Photovoltaic (PV)
Photovoltaic definition- a material or device that is capable of converting the energy contained in photons of light into an electrical voltage and current
Solar cells are diodes, creating dc power, which in grid applications is converted to ac by an inverter
For terrestrial applications, the capacity factor is limited by night, relative movement of the sun, the atmosphere, clouds, shading, etc.
  A ballpark figure for Texas is about 25%; US high of about 29%, some states go below 17%
  "One sun" is defined a 1 kw/m2,which is the maximum insolation the reaches the surface of the earth (sun right overhead)
43

## Slide 45: The Sun as a Resource
In space the amount of solar radiation (i.e., sunlight) just depends on the distance from the sun, with a 100% capacity factor
On earth the amount of solar radiation (i.e., sunlight) available at a location depends on many things, and varies significantly because of atmospheric attenuation
44

## Slide 46: Solar Radiation versus Irradiance
Various terms are used to describe the energy emitted by the sun
Solar radiation refers to the total energy emitted by the sun (visible, infrared, ultraviolet), and is mostly used in scientific fields
Solar irradiance refers to the amount of energy received (e.g., watts per square meter), and is used more in engineering
  The terms solar insolation or just insolation are also used
With solar PV there are several standard values
  Direct normal irradiance (DNI) is the amount of power received on a surface perpendicular to the sun
  Diffuse horizontal irradiance (DHI) is the amount of power received from light scattering
  Global horizontal irradiance (GHI) is the total amount on a horizontal surface
45

## Slide 47: US Global Horizontal Irradiance (GHI)
The capacity factor is usually about 1.25 times this number divided by 24 hours per day
46

## Slide 48: Worldwide Annual Insolation
47

## Slide 49: Solar Photovoltaics (PV)
Photovoltaics is the conversion of light into electricity using semiconductors known as solar cells
  It dates back to 1883, but really got going in the late 1950’s, driven by NASA
  Solar cells produce a dc output, with the right image showing an example IV curve
Solar modules are groups of solar cells; a PV panel is one or more modules wired together ready to mount
A PV system often includes an inverter to produce ac electricity
PV panels can either have a fixed mount, or be on a tracker; trackers can be one-axis or two-axis
48